Names: Tam A. Luong and Sartrapat Saengcharoentrakul
Usernames: tluong04 and ssaeng01
Assignment 7
Labnotes

Files chosen for benchmarks:
small benchmark: midmark.um
big benchmark: advent.umz (with "n", "take bolt", and "quit" as input)

Benchmark	Time	Instructions	Relative to start	Relative to previous	Improvement
Big	66.313	-	1.000	1.000	No improvement (starting point)
Small	8.176	8.0 x 10^7	1.000	1.000
Big	50.039	-	0.755	0.755	Compiled with Optimization turned on and linked against -lcii-01
Small	6.157	8.0 x 10^7	0.753	0.753
Big	44.416	-	0.670	0.888	Compiled with Optimization turned on and linked against -lcii-02
Small	5.484	8.0 x 10^7	0.671	0.891
Big	39.543	-	0.596	0.891	Eliminate bitpack_getu() for opcode 0-12
Small	4.976	53,521,922,710	0.609	0.907
Big	37.555	-	0.567	0.950	Eliminate bitpack_getu() for opcode 13
Small	4.661	53,521,922,710	0.571	0.937
Big	33.805	-	0.510	0.900	Eliminate the use of progCounter functions
Small	4.241	36,393,384,141	0.519	0.910
Big	29.184	-	0.440	0.863	Changed the segment implementation from UArray to C-Array
Small	3.586	31,043,724,017	0.439	0.846
Big	24.006	-	0.362	0.823	Change the register implementation from Uarray to C-Array
Small	3.048	26,460,977,863	0.373	0.850
Big	22.349		0.337	0.931	Replace register_get() and register_put() with direct c-array access
Small	2.839	23,443,685,796	0.347	0.931
Big	17.085	-	0.258	0.764	Replace segment_isEmpty() with direct access
Small	2.170	18,313,839,202	0.265	0.764
Big	10.130	-	0.153	0.593	Replace segment_length() with direct access
Small	1.339	8,897,436,767	0.164	0.617
Big	9.772	-	0.147	0.965	Replace segment_get with direct memory access
Small	1.262	8,609,926,252	0.154	0.942
Big		-
Small		53,521,922,710
Big		-
Small		53,521,922,710
Big		-
Small		53,521,922,710

First Valgrind run:
11602
First Improvement:
We noticed that a lot of time is spent in Bitpack_getu,

Second Valgrind run:
4590
We noticed that Uarray_at takes up a lot of of time, with 26.88%. So we decide to change the segment implementation from Uarray to CArray

Third Valgrind run:
8410
We noticed that Uarray_at still takes a lot of time so we decided to change the register implementation from Uarray to Carray too.

Forth Valgrind run:
9929
We noticed that register_get() and register_put() take a significant time to run. So we decided to replace these functions with direct memory access/

Fifth Valgrind run:
11023
We noticed that Segment_isEmpty takes a lot of time. Hence we decided to replace the function with direct memory access from the memory

Sixth Valgrind run:
11575
We noticed that Segment_length takes a lot of time.

Seventh Valgrind run:
5773
We noticed that segment_get still takes up a big portion of the running time. We will try to remove segment_get as well.

Eighth Valgrind run:
6734